## Slide 1: RingCentral Layer-2 Inline QoS Device

## Slide 2: Issue to be Resolved
Many simple customer sites connect the customer’s local network directly to an ISP’s gateway device.
Many of these ISP gateway devices have no provision or capability to implement QoS and Traffic Shaping.
ISP
Gateway
Customer
Network

## Slide 3: Solution
Insert a device between the ISP’s gateway device and the Customer network.
Operate transparently as a layer-2 bridge.
ISP
Gateway
Customer
Network
Layer-2 Inline
QoS Device

## Slide 4: Solution
Examine traffic, classify it, and mark the traffic’s class.
  Voice – highest priority (large amount of traffic)
  Video – next highest priority (very large amount of traffic)
  Signaling – next highest priority (small amount of traffic)
  Other RingCentral traffic
  Other traffic
Upon egress, apply traffic shaping rules described in the next slide.

## Slide 5: Solution (continued)
Traffic Shaping Rules
  Hierarchical Token Bucket (HTB) Queue Tree
  Define absolute maximum limit of upstream bandwidth to ISP. Best practice is to use a value that is 95% of the contracted ISP rate.
  Each class has a minimum guaranteed data rate.
  Classes’ unused bandwidth is handed out to other classes as needed but returned immediately when needed.

## Slide 6: Solution (continued)
Hardware
  Mikrotik (a Latvian company formed in 1996) Routers and Access Points.
    Very high performance at commodity prices
    hEX PoE offers 1 SFP, 1 non-PoE GigabitEthernet, and 4 PoE GigabitEthernet ports for under US$90.00 MSRP.
    hAP ac offers integral dual band wireless, 1 SFP, 4 non-PoE GigabitEthernet, and 1 PoE GigabitEthernet ports for under US$129.00 MSRP.

## Slide 7: Technical Background
The Mikrotik Router’s ports are placed into a bridge configuration, but Layer-3 firewall rules are applied for connection/packet classification.
Port ether1 is connected to the upstream ISP’s gateway device.
All other ports, including WiFi devices, are dedicated to customer network connections.
All new connections are classified upon ingress.
All packets related to a connection are marked with the correct class.

## Slide 8: Technical Background (continued)
The Mikrotik Router’s ports are placed into a bridge configuration, but Layer-3 firewall rules are applied for connection/packet classification.
Port ether1 is connected to the upstream ISP’s gateway device.
All other ports, including integral WiFi devices, are dedicated to customer network connections.
All new connections are classified upon ingress.
All packets related to a connection are marked with the correct class upon ingress. (DSCP tag, priority tag)

## Slide 9: Technical Background (continued)
Traffic egressing to integral WiFi devices has priority altered to properly classify in WMM
Traffic Shaping is applied to all ports to force prioritization based upon class.
Traffic Shaping to the ISP’s gateway device (ether1) is shaped to a set output bandwidth with guaranteed minimum allocations for each class.

## Slide 10: Technical Background (continued)
The logical bridge device has an assigned dummy layer-3 IP address which is unused but required by the software.
Management access is accomplished using the Mikrotik WinBox software to connect directly via MAC address.
All traffic MUST pass through the Inline QoS Device, nothing else can be connected to the ISP’s gateway device.